## Slide 1: Computer Architecture
Lab 5: Building Blocks of Processor

## Slide 2: Getting Started
Open a web browser and go to https://www.edaplayground.com/

## Slide 3: Lab Assignment 1: ALU
Write a SystemVerilog code to implement the ALU
  Its functionality is given in the table on the right.
  Additional requirement: the ALU should generate a signal that indicates whether the result is zero or not
The ALU has the following inputs and outputs
  iA (32 bits): source operand 1
  iB (32 bits): source operand 2
  iF (3 bits): control signal
  oY (32 bits): result
  oZero (1 bit): 1 if oY==0, 0 otherwise
Use the testbench in the following slide
Submit your code as plain text to Blackboard
iF2:0 | Function
000 | iA & iB
001 | iA ¦ iB
010 | iA + iB
011 | not used
100 | iA & ~iB
101 | iA ¦ ~iB
110 | iA – iB
111 | SLT

## Slide 4: Testbench for ALU
module testbench_alu();
logic [31:0] a, b, y;
logic [2:0] f;
logic zero;
logic result;
alu dut(
.iA (a),
.iB (b),
.iF (f),
.oY (y),
.oZero (zero)
);
initial begin
$dumpfile("dump.vcd"); $dumpvars;
result = 1'b1;
a = 32'h1234_5678; b = 32'h0000_ffff; f=3'b000; #10;
if(y!=32'h0000_5678) begin $display("000 failed."); result=1'b0; end
a = 32'h1234_5678; b = 32'h0000_ffff; f=3'b001; #10;
if(y!=32'h1234_ffff) begin $display("001 failed."); result=1'b0; end
a = 32'h1234_5678; b = 32'h1111_2222; f=3'b010; #10;
if(y!=32'h2345_789a) begin $display("010 failed."); result=1'b0; end
a = 32'h1234_5678; b = 32'h0000_ffff; f=3'b100; #10;
if(y!=32'h1234_0000) begin $display("100 failed."); result=1'b0; end
a = 32'h1234_5678; b = 32'h0000_ffff; f=3'b101; #10;
if(y!=32'hffff_5678) begin $display("101 failed."); result=1'b0; end
a = 32'h1234_5678; b = 32'h1111_2222; f=3'b110; #10;
if(y!=32'h0123_3456) begin $display("110 failed."); result=1'b0; end
a = 32'h0000_5678; b = 32'h0000_ffff; f=3'b111; #10;
if(y!=32'h0000_0001) begin $display("111 failed."); result=1'b0; end
a = 32'h0000_0000; b = 32'h0000_0000; f=3'b000; #10;
if(zero!=1) begin $display("zero failed."); result=1'b0; end
if(result) $display("SUCCESS!");
else $display("FAILURE!");
end
endmodule

## Slide 5: Lab Assignment 2: Register File
Write a SystemVerilog code to implement a register file
It has 32 32-bit registers and the register 0 should be always 0
It has two read ports and one write port
It has the following inputs and outputs
  iClk (1 bit): clock (rising edge)
  iReset (1 bit): reset signal
  iRaddr1 (5 bits): the register number of read port 1
  oRdata1 (32 bits): the output of read port 1
  iRaddr2 (5 bits): the register number of read port 2
  oRdata2 (32 bits): the output of read port 2
  iWaddr (5 bits): the register number of the write port
  iWdata (32 bits): the input data for the write port
  iWe (1 bit): the write enable signal
Use the testbench in the following slide
Submit your code as plain text to Blackboard

## Slide 6: Testbench for Register File
module testbench_regfile();
logic clk;
logic reset;
logic [4:0] raddr1, raddr2, waddr;
logic we;
logic [31:0] wdata;
logic [31:0] rdata1, rdata2;
logic result;
logic [31:0] regs[31:0];
integer i;
regfile dut(
.iClk (clk),
.iReset (reset),
.iRaddr1(raddr1),
.iRaddr2(raddr2),
.iWaddr (waddr),
.iWe (we),
.iWdata (wdata),
.oRdata1(rdata1),
.oRdata2(rdata2)
);
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5;
end
initial begin
result = 1;
$dumpfile("dump.vcd"); $dumpvars;
reset = 0; #21;
raddr1 = 0; raddr2 = 0; waddr = 0; we = 0; wdata = 0;
for(i=0; i<32; i=i+1) regs[i]=0;
reset = 1; #10;
reset = 0; #10;
for(i=0; i<32; i=i+1) begin
waddr = i; we = 1; wdata = $random; regs[i] = wdata; #10;
end
waddr = 0; we = 0; wdata = 0;
for(i=0; i<32; i=i+1) begin
raddr1 = i; raddr2 = i; #1
if(i==0) begin
if(rdata1 != 0 | rdata2 != 0) begin
$display("Read data from r0 failed");
result = 0;
end
end else begin
if(rdata1 != regs[i]) begin
$display("Read data from port 1 at address %d failed %x %x", i, rdata1, regs[i]);
result = 0;
end
if(rdata2 != regs[i]) begin
$display("Read data from port 2 at address %d failed", i);
result = 0;
end
end
#9;
end
if(result) $display("SUCCESS!");
else $display("FAILURE!");
#10; $stop;
end
endmodule