## Slide 1: Computer Architecture
Lab 6: Datapath

## Slide 2: Getting Started
Download alu.sv, regfile.sv, imem.sv and dmem.sv from Blackboard
Open a web browser and go to https://www.edaplayground.com/

## Slide 3: Structural Modeling - Hierarchy
module and3(input logic a, b, c,
output logic y);
assign y = a & b & c;
endmodule
module inv(input logic a,
output logic y);
assign y = ~a;
endmodule
module nand3(input logic a, b, c
output logic y);
logic n1; // internal signal
and3 andgate(a, b, c, n1); // instance of and3
inv inverter(n1, y); // instance of inverter
endmodule

## Slide 4: Structural Modeling – Better Way
module and3(input logic a, b, c,
output logic y);
assign y = a & b & c;
endmodule
module inv(input logic a,
output logic y);
assign y = ~a;
endmodule
module nand3(input logic a, b, c
output logic y);
logic n1;
and3 andgate(
.a (a),
.b (b),
.c (c),
.y (n1)
);
inv inverter(
.a (n1),
.y (y)
);
endmodule

## Slide 5: Datapath for lw Instruction

## Slide 6: Testbench
Copy the following testbench code to “testbench.sv” on the left
module testbench_lw();
logic clk;
logic reset;
logic regwrite;
logic memwrite;
logic [2:0] alucontrol;
datapath dut(
.iClk (clk),
.iReset (reset),
.iRegWrite (regwrite),
.iMemWrite (memwrite),
.iALUControl(alucontrol)
);
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5;
end
initial begin
$dumpfile("dump.vcd"); $dumpvars;
reset = 0; #21;
reset = 1; #10;
regwrite = 1; memwrite = 0; alucontrol = 3'b010;
reset = 0; #10;
#10; $stop;
end
endmodule

## Slide 7: Datapath
Copy the following code to “design.sv” on the right
`include "alu.sv"
`include "regfile.sv"
`include "imem.sv"
`include "dmem.sv"
module datapath(
input logic iClk,
input logic iReset,
input logic iRegWrite,
input logic iMemWrite,
input logic [2:0] iALUControl
);
endmodule

## Slide 8: Building Blocks
Click “+” right after “design.sv”
Upload “alu.sv”
Upload regfile.sv, imem.sv, and dmem.sv in the same way

## Slide 9: Lab Assignment
Finish the implementation of the datapath module
  Implement the program counter and sign extension
  Connect modules
Save and submit the link of your design to the Blackboard.

## Slide 10: Expected Result