## Slide 1: Computer Architecture
Chapter 7: Microarchitecture
Largely based on slides by David and Sarah Harris

## Slide 2: Chapter 7 Topics
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Exceptions
Advanced Microarchitecture

## Slide 3: Introduction
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals

## Slide 4: Microarchitecture
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once

## Slide 5: Processor Performance
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: Cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle = IPC
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance

## Slide 6: Exercise 1
What is CPI (cycle per instruction) if
  The execution time is 1 ms
  The number of instructions is 100,000
  The clock speed is 1 GHz

## Slide 7: Exercise 1
What is CPI (cycle per instruction) if
  The execution time is 1 ms
  The number of instructions is 100,000
  The clock speed is 1 GHz
  1 ms = 100,000 x CPI x 1 ns
  (1 x 10-3) = (1 x 105) x CPI x (1 x 10-9)
  CPI = 10-3-5+9 = 10 (instruction/cycle)

## Slide 8: Architectural State
Determines everything about a processor:
  PC
  32 registers
  Memory

## Slide 9: MIPS State Elements

## Slide 10: Single-Cycle MIPS Processor
Datapath
Control

## Slide 11: Single-Cycle Datapath: lw fetch
STEP 1: Fetch instruction

## Slide 12: Single-Cycle Datapath: lw Register Read
STEP 2: Read source operands from RF

## Slide 13: Single-Cycle Datapath: lw Immediate
STEP 3: Sign-extend the immediate

## Slide 14: Single-Cycle Datapath: lw address
STEP 4: Compute the memory address

## Slide 15: Single-Cycle Datapath: lw Memory Read
STEP 5: Read data from memory and write it back to register file

## Slide 16: Single-Cycle Datapath: lw PC Increment
STEP 6: Determine address of next instruction

## Slide 17: Single-Cycle Datapath: sw
Write data in rt to memory

## Slide 18: Exercise 2
Show the value of signals on the datapath of the following single-cycle processor. The current value of registers and memory is given in the following tables.
Register | Value
0 ($0) | 0x00000000
… | 
8 ($t0) | 0x00001000
9 ($t1) | 0x00000000
… | 
$pc | 0x00002000
Memory address | Value
0x00001000 | 0x12345678
0x00001004 | 0x00000000
0x00001008 | 0x00000000
… | 
0x00002000 | 0x8D090000
0x00002004 | 0xAD090004

## Slide 19: Exercise 2
0x00002000
0x00002004
0x8D090000
0x8
0x9
0x00001000
0x0000
0x00000000
0x00001000
0x12345678
Register | Value
0 ($0) | 0x00000000
… | 
8 ($t0) | 0x00001000
9 ($t1) | 0x00000000
… | 
$pc | 0x00002000
Memory address | Value
0x00001000 | 0x12345678
0x00001004 | 0x00000000
0x00001008 | 0x00000000
… | 
0x00002000 | 0x8D090000
0x00002004 | 0xAD090004

## Slide 20: Exercise 2
0x00002004
0x00002008
0xAD090004
0x8
0x9
0x00001000
0x0004
0x00000004
0x00001004
0x12345678
Register | Value
0 ($0) | 0x00000000
… | 
8 ($t0) | 0x00001000
9 ($t1) | 0x12345678
… | 
$pc | 0x00002004
Memory address | Value
0x00001000 | 0x12345678
0x00001004 | 0x00000000
0x00001008 | 0x00000000
… | 
0x00002000 | 0x8D090000
0x00002004 | 0xAD090004

## Slide 21: Single-Cycle Datapath: R-Type
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)

## Slide 22: Review: Instruction Formats

## Slide 23: Exercise 3
Show the value of signals on the datapath of the following single-cycle processor. The current value of registers and memory is given in the following tables.
Instruction @ 0x00003000
= 0x00084820
add $t1, $0, $t0
Register | Value
0 ($0) | 0x00000000
… | 
8 ($t0) | 0x00001234
9 ($t1) | 0x00000000
… | 
$pc | 0x00003000

## Slide 24: Exercise 3
0x00003000
0x00003004
0x00084820
0x0
0x8
0x8
0x9
0x00000000
0x00001234
0x00001234
0x00001234
0x00001234
Register | Value
0 ($0) | 0x00000000
… | 
8 ($t0) | 0x00001234
9 ($t1) | 0x00000000
… | 
$pc | 0x00003000

## Slide 25: Single-Cycle Datapath: beq
Determine whether values in rs and rt are equal
Calculate branch target address:
BTA = (sign-extended immediate << 2) + (PC+4)

## Slide 26: Single-Cycle Processor

## Slide 27: Single-Cycle Control

## Slide 28: Review: ALU
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 29: Review: ALU

## Slide 30: Control Unit: ALU Decoder
ALUOp1:0 | Meaning
00 | Add
01 | Subtract
10 | Look at Funct
11 | Not Used
ALUOp1:0 | Funct | ALUControl2:0
00 | X | 010 (Add)
X1 | X | 110 (Subtract)
1X | 100000 (add) | 010 (Add)
1X | 100010 (sub) | 110 (Subtract)
1X | 100100 (and) | 000 (And)
1X | 100101 (or) | 001 (Or)
1X | 101010 (slt) | 111 (SLT)

## Slide 31: Control Unit: Main Decoder
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 |  |  |  |  |  |  | 
lw | 100011 |  |  |  |  |  |  | 
sw | 101011 |  |  |  |  |  |  | 
beq | 000100 |  |  |  |  |  |  | 

## Slide 32: Control Unit: Main Decoder
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01

## Slide 33: Single-Cycle Datapath: or

## Slide 34: Extended Functionality: addi
No change to datapath

## Slide 35: Control Unit: addi
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 |  |  |  |  |  |  | 

## Slide 36: Control Unit: addi
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00

## Slide 37: Extended Functionality: j

## Slide 38: Control Unit: j
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 |  |  |  |  |  |  |  | 

## Slide 39: Control Unit: j
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 | 0 | X | X | X | 0 | X | XX | 1

## Slide 40: Review: Processor Performance
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC

## Slide 41: Single-Cycle Performance
TC limited by critical path (lw)

## Slide 42: Single-Cycle Performance
Single-cycle critical path:
Tc = tpcq_PC + tmem + max(tRFread, tsext + tmux) + tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup

## Slide 43: Exercise 1
Tc = ?
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20

## Slide 44: Exercise 1
Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
= [30 + 2(250) + 150 + 25 + 200 + 20] ps
= 925 ps
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20

## Slide 45: Example
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC = (100 × 109)(1)(925 × 10-12 s) = 92.5 seconds

## Slide 46: Pipelined MIPS Processor
Temporal parallelism
Divide single-cycle processor into 5 stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback
Add pipeline registers between stages

## Slide 47: Single-Cycle vs. Pipelined

## Slide 48: Pipelined Processor Abstraction

## Slide 49: Single-Cycle & Pipelined Datapath

## Slide 50: Corrected Pipelined Datapath
WriteReg must arrive at same time as Result

## Slide 51: Pipelined Processor Control
Same control unit as single-cycle processor
Control delayed to proper pipeline stage

## Slide 52: Pipeline Hazards
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file
  Control hazard: next instruction not decided yet (caused by branches)

## Slide 53: Data Hazard

## Slide 54: Handling Data Hazards
Insert nops in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time

## Slide 55: Compile-Time Hazard Elimination
Insert enough nops for result to be ready
Or move independent useful instructions forward

## Slide 56: Data Forwarding

## Slide 57: Data Forwarding

## Slide 58: Data Forwarding
Forward to Execute stage from either:
  Memory stage or
  Writeback stage
Forwarding logic for ForwardAE :
if ((rsE != 0) AND (rsE == WriteRegM) AND RegWriteM)
then ForwardAE = 10
else if ((rsE != 0) AND (rsE == WriteRegW) AND RegWriteW)
then ForwardAE = 01
else ForwardAE = 00
Forwarding logic for ForwardBE same, but replace rsE with rtE

## Slide 59: Stalling

## Slide 60: Stalling

## Slide 61: Stalling Hardware

## Slide 62: Stalling Logic
lwstall =
((rsD==rtE) OR (rtD==rtE)) AND MemtoRegE
StallF = StallD = FlushE = lwstall

## Slide 63: Exercise 1
For 5-stage pipelined processor, mark which stage the processor is in for each instruction. If data forwarding happens, mark it as an arrow from its source to destination. Note that if stalling happens, the affected instruction should remain in the same stage for one more cycle.
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
lw $t0, 0($0)
lw $t1, 4($0)
add $t2, $t1, $t2
addi $t3, $t2, 4

## Slide 64: Exercise 1
For 5-stage pipelined processor, mark which stage the processor is in for each instruction. If data forwarding happens, mark it as an arrow from its source to destination. Note that if stalling happens, the affected instruction should remain in the same stage for one more cycle.
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | D | E | M | W |  | 
 |  |  | F | F | D | E | M | W | 
lw $t0, 0($0)
lw $t1, 4($0)
add $t2, $t1, $t2
addi $t3, $t2, 4

## Slide 65: Control Hazards
beq:
  branch not determined until 4th stage of pipeline
  Instructions after branch fetched before branch occurs
  These instructions must be flushed if branch happens
Branch misprediction penalty
  number of instruction flushed when branch is taken
  May be reduced by determining branch earlier

## Slide 66: Control Hazards: Original Pipeline

## Slide 67: Control Hazards

## Slide 68: Early Branch Resolution

## Slide 69: Early Branch Resolution
Introduced another data hazard in Decode stage

## Slide 70: Handling Data & Control Hazards

## Slide 71: Control Forwarding & Stalling Logic
Forwarding logic:
ForwardAD = (rsD !=0) AND (rsD == WriteRegM) AND RegWriteM
ForwardBD = (rtD !=0) AND (rtD == WriteRegM) AND RegWriteM
Stalling logic:
branchstall = BranchD AND RegWriteE AND
(WriteRegE == rsD OR WriteRegE == rtD)
OR
BranchD AND MemtoRegM AND
(WriteRegM == rsD OR WriteRegM == rtD)
StallF = StallD = FlushE = lwstall OR branchstall

## Slide 72: Branch Prediction
Guess whether branch will be taken
  Backward branches are usually taken (loops)
  Consider history to improve guess
Good prediction reduces fraction of branches requiring a flush

## Slide 73: Exercise 2
For 5-stage pipelined processor, mark which stage the processor is in for each instruction. If data forwarding happens, mark it as an arrow from its source to destination. Note that if stalling happens, the affected instruction should remain in the same stage for one more cycle. If an instruction is fetched but flushed, mark it with X.
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
20: add $t0, $0, $0
24: add $t1, $0, $0
28: beq $t0, $t1, 38
2C: beq $t0, $0, 80
30: beq $t1, $0, 90
...
64: lw $t2, 0($t1)

## Slide 74: Exercise 2
For 5-stage pipelined processor, mark which stage the processor is in for each instruction. If data forwarding happens, mark it as an arrow from its source to destination. Note that if stalling happens, the affected instruction should remain in the same stage for one more cycle. If an instruction is fetched but flushed, mark it with X.
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | D | E | M | W |  | 
 |  |  |  | F | D | E | M | W | 
 |  |  |  |  | F | D | E | M | W
20: add $t0, $0, $0
24: add $t1, $0, $0
28: beq $t0, $t1, 38
2C: beq $t0, $0, 80
30: beq $t1, $0, 90
...
64: lw $t2, 0($t1)

## Slide 75: Pipelined Performance Example
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Suppose:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
What is the average CPI?

## Slide 76: Pipelined Performance Example
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Suppose:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
What is the average CPI?
  Load/Branch CPI = 1 when no stalling, 2 when stalling
  CPIlw = 1(0.6) + 2(0.4) = 1.4
  CPIbeq = 1(0.75) + 2(0.25) = 1.25
  Average CPI = (0.25)(1.4) + (0.1)(1) + (0.11)(1.25) + (0.02)(2) + (0.52)(1)
  = 1.15

## Slide 77: Pipelined Processor
Tc = 2(tRFread + tmux + teq + tAND + tmux + tsetup )

## Slide 78: Pipelined Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Equality comparator | teq | 40
AND gate | tAND | 15
Memory write | Tmemwrite | 220
Register file write | tRFwrite | 100 ps
Tc = 2(tRFread + tmux + teq + tAND + tmux + tsetup )
= 2[150 + 25 + 40 + 15 + 25 + 20] ps = 550 ps

## Slide 79: Pipelined Performance Example
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc = (100 × 109)(1.15)(550 × 10-12) = 63 seconds

## Slide 80: Processor Performance Comparison
Processor | Execution Time (seconds) | Speedup (single-cycle as baseline)
Single-cycle | 92.5 | 1
Multicycle | 133 | 0.70
Pipelined | 63 | 1.47

## Slide 81: Exceptions
Unscheduled function call to exception handler
Caused by:
  Hardware, also called an interrupt, e.g. keyboard
  Software, also called traps, e.g. undefined instruction
When exception occurs, the processor:
  Records cause of exception (Cause register)
  Jumps to exception handler (0x80000180)
  Returns to program (EPC register)

## Slide 82: Example Exception

## Slide 83: Exception Registers
Not part of register file
  Cause
    Records cause of exception
    Coprocessor 0 register 13
  EPC (Exception PC)
    Records PC where exception occurred
    Coprocessor 0 register 14
Move from Coprocessor 0
  mfc0 $t0, Cause
  Moves contents of Cause into $t0

## Slide 84: Exception Causes
Exception | Cause
Hardware Interrupt | 0x00000000
System Call | 0x00000020
Breakpoint / Divide by 0 | 0x00000024
Undefined Instruction | 0x00000028
Arithmetic Overflow | 0x00000030
Extend multicycle MIPS processor to handle last two types of exceptions

## Slide 85: Exception Hardware: EPC & Cause

## Slide 86: Exception Hardware: mfc0

## Slide 87: Deep Pipelining
10-20 stages typical
Number of stages limited by:
  Pipeline hazards
  Sequencing overhead
  Power
  Cost

## Slide 88: Branch Prediction
Ideal pipelined processor: CPI = 1
Branch misprediction increases CPI
Static branch prediction:
  Check direction of branch (forward or backward)
  If backward, predict taken
  Else, predict not taken
Dynamic branch prediction:
  Keep history of last (several hundred) branches in branch target buffer, record:
    Branch destination
    Whether branch was taken

## Slide 89: Branch Prediction Example
add $s1, $0, $0 # sum = 0
add $s0, $0, $0 # i = 0
addi $t0, $0, 10 # $t0 = 10
for:
beq $s0, $t0, done # if i == 10, branch
add $s1, $s1, $s0 # sum = sum + i
addi $s0, $s0, 1 # increment i
j for
done:

## Slide 90: 1-Bit Branch Predictor
Remembers whether branch was taken the last time and does the same thing
Mispredicts first and last branch of loop

## Slide 91: 2-Bit Branch Predictor
Only mispredicts last branch of loop

## Slide 92: Superscalar
Multiple copies of datapath execute multiple instructions at once
Dependencies make it tricky to issue multiple instructions at once

## Slide 93: Superscalar Example
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 2
or $t3, $s5, $s6
sw $s7, 80($t3)

## Slide 94: Superscalar with Dependencies
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/5 = 1.17
or $t3, $s5, $s6
sw $s7, 80($t3)

## Slide 95: Out of Order Processor
Looks ahead across multiple instructions
Issues as many instructions as possible at once
Issues instructions out of order (as long as no dependencies)
Dependencies:
  RAW (read after write): one instruction writes, later instruction reads a register
  WAR (write after read): one instruction reads, later instruction writes a register
  WAW (write after write): one instruction writes, later instruction writes a register

## Slide 96: Out of Order Processor
Instruction level parallelism (ILP): number of instruction that can be issued simultaneously (average < 3)
Scoreboard: table that keeps track of:
  Instructions waiting to issue
  Available functional units
  Dependencies

## Slide 97: Out of Order Processor Example
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/4 = 1.5
or $t3, $s5, $s6
sw $s7, 80($t3)

## Slide 98: Register Renaming
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/3 = 2
or $t3, $s5, $s6
sw $s7, 80($t3)

## Slide 99: SIMD
Single Instruction Multiple Data (SIMD)
  Single instruction acts on multiple pieces of data at once
  Common application: graphics
  Perform short arithmetic operations (also called packed arithmetic)
For example, add four 8-bit elements

## Slide 100: Advanced Architecture Techniques
Multithreading
  Wordprocessor: thread for typing, spell checking, printing
Multiprocessors
  Multiple processors (cores) on a single chip

## Slide 101: Threading: Definitions
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing

## Slide 102: Threads in Conventional Processor
One thread runs at once
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching
Appears to user like all threads running simultaneously

## Slide 103: Multithreading
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”

## Slide 104: Multiprocessors
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system

## Slide 105: Other Resources
Patterson & Hennessy’s: Computer Architecture: A Quantitative Approach
Conferences:
  ISCA (International Symposium on Computer Architecture)
  HPCA (International Symposium on High Performance Computer Architecture)
  MICRO (International Symposium on Microarchitecture)