## Slide 1: Computer Architecture
Chapter 8: Memory and I/O Systems
Largely based on slides by David and Sarah Harris

## Slide 2: Chapter 8 Topics
Memory System Performance Analysis
Caches
Virtual Memory
Memory-Mapped I/O

## Slide 3: Introduction
Computer performance depends on:
  Processor performance
  Memory system performance
Memory Interface

## Slide 4: Processor-Memory Gap
In prior chapters, assumed access memory in 1 clock cycle – but hasn’t been true since the 1980’s

## Slide 5: Memory System Challenge
Make memory system appear as fast as processor
Use hierarchy of memories
Ideal memory:
  Fast
  Cheap (inexpensive)
  Large (capacity)
But can only choose two!

## Slide 6: Memory Hierarchy

## Slide 7: Locality
Exploit locality to make memory accesses fast
Temporal Locality:
  Locality in time
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space
  If data used recently, likely to use nearby data soon
  How to exploit: when access data, bring nearby data into higher levels of memory hierarchy too

## Slide 8: Memory Performance
Hit: data found in that level of memory hierarchy
Miss: data not found (must go to next level)
Hit Rate = # hits / # memory accesses
= 1 – Miss Rate
Miss Rate = # misses / # memory accesses
= 1 – Hit Rate
Average memory access time (AMAT): average time for processor to access data
AMAT = tcache + MRcache[tMM + MRMM(tVM)]

## Slide 9: Memory Performance Example 1
A program has 2,000 loads and stores
1,250 of these data values in cache
Rest supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?

## Slide 10: Memory Performance Example 1
A program has 2,000 loads and stores
1,250 of these data values in cache
Rest supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?
Hit Rate = 1250/2000 = 0.625
Miss Rate = 750/2000 = 0.375 = 1 – Hit Rate

## Slide 11: Memory Performance Example 2
Suppose processor has 2 levels of hierarchy: cache and main memory
tcache = 1 cycle, tMM = 100 cycles
What is the AMAT of the program from Example 1?

## Slide 12: Memory Performance Example 2
Suppose processor has 2 levels of hierarchy: cache and main memory
tcache = 1 cycle, tMM = 100 cycles
What is the AMAT of the program from Example 1?
AMAT = tcache + MRcache(tMM)
= [1 + 0.375(100)] cycles
= 38.5 cycles

## Slide 13: Cache
Highest level in memory hierarchy
Fast (typically ~ 1 cycle access time)
Ideally supplies most data to processor
Usually holds most recently accessed data

## Slide 14: Cache Design Questions
What data is held in the cache?
How is data found?
What data is replaced?
Focus on data loads, but stores follow same principles

## Slide 15: What data is held in the cache?
Ideally, cache anticipates needed data and puts it in cache
But impossible to predict future
Use past to predict future – temporal and spatial locality:
  Temporal locality: copy newly accessed data into cache
  Spatial locality: copy neighboring data into cache too

## Slide 16: Cache Terminology
Capacity (C):
  number of data bytes in cache
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 17: How is data found?
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by # of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks in 1 set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)

## Slide 18: Example Cache Parameters
C = 8 words (capacity)
b = 1 word (block size)
So, B = 8 (# of blocks)
Ridiculously small, but will illustrate organizations

## Slide 19: Direct Mapped Cache

## Slide 20: Direct Mapped Cache Hardware

## Slide 21: Example 1
Mark hit (H) or miss (M) for each load instruction assuming a direct mapped cache whose size is 8 words (32 bytes) and block size is one word (4 bytes)
    lb 0x00 (00000000)
    lb 0x01 (00000001)
    lb 0x22 (00100010)
    lb 0x2B (00101011)
    lb 0x02 (00000010)
    lb 0x29 (00101001)

## Slide 22: Example 1
Mark hit (H) or miss (M) for each load instruction assuming a direct mapped cache whose size is 8 words (32 bytes) and block size is one word (4 bytes)
    lb 0x00 (00000000) M
    lb 0x01 (00000001) H
    lb 0x22 (00100010) M
    lb 0x2B (00101011) M
    lb 0x02 (00000010) M
    lb 0x29 (00101001) H

## Slide 23: Exercise 1
For the following direct mapped cache configurations, which parts of the address bits are for tag, index and offset?
Block size | Total size | Tag | Index | Offset
4 bytes | 32 bytes |  |  | 
8 bytes | 64 bytes |  |  | 
4 bytes | 64 bytes |  |  | 

## Slide 24: Exercise 1
For the following direct mapped cache configurations, which parts of the address bits are for tag, index and offset?
Block size | Total size | Tag | Index | Offset
4 bytes | 32 bytes | [31:5] | [4:2] | [1:0]
8 bytes | 64 bytes | [31:6] | [5:3] | [2:0]
4 bytes | 64 bytes | [31:6] | [5:2] | [1:0]

## Slide 25: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?

## Slide 26: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15
= 20%
Compulsory Misses

## Slide 27: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?

## Slide 28: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10
= 100%

## Slide 29: N-Way Set Associative Cache

## Slide 30: N-Way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?

## Slide 31: N-Way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces
conflict misses

## Slide 32: Fully Associative Cache
Reduces conflict misses
Expensive to build

## Slide 33: Example 2
Mark hit (H) or miss (M) for each load instruction assuming a 2-way associative cache whose size is 8 words (32 bytes) and block size is one word (4 bytes)
    lb 0x00 (00000000)
    lb 0x01 (00000001)
    lb 0x22 (00100010)
    lb 0x2B (00101011)
    lb 0x02 (00000010)
    lb 0x29 (00101001)

## Slide 34: Example 2
Mark hit (H) or miss (M) for each load instruction assuming a 2-way associative cache whose size is 8 words (32 bytes) and block size is one word (4 bytes)
    lb 0x00 (00000000) M
    lb 0x01 (00000001) H
    lb 0x22 (00100010) M
    lb 0x2B (00101011) M
    lb 0x02 (00000010) H
    lb 0x29 (00101001) H

## Slide 35: Exercise 2
For the following 2-way associative cache configurations, which parts of the address bits are for tag, index and offset?
Block size | Total size | Tag | Index | Offset
4 bytes | 32 bytes |  |  | 
8 bytes | 64 bytes |  |  | 
4 bytes | 64 bytes |  |  | 

## Slide 36: Exercise 2
For the following 2-way associative cache configurations, which parts of the address bits are for tag, index and offset?
Block size | Total size | Tag | Index | Offset
4 bytes | 32 bytes | [31:4] | [3:2] | [1:0]
8 bytes | 64 bytes | [31:5] | [4:3] | [2:0]
4 bytes | 64 bytes | [31:5] | [4:2] | [1:0]

## Slide 37: Spatial Locality?
Increase block size:
  Block size, b = 4 words
  C = 8 words
  Direct mapped (1 block per set)
  Number of blocks, B = 2 (C/b = 8/4 = 2)

## Slide 38: Cache with Larger Block Size

## Slide 39: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?

## Slide 40: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 1/15
= 6.67%
Larger blocks
reduce compulsory misses
through spatial locality

## Slide 41: Cache Organization Recap
Capacity: C
Block size: b
Number of blocks in cache: B = C/b
Number of blocks in a set: N
Number of sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1

## Slide 42: Capacity Misses
Cache is too small to hold all data of interest at once
If cache full: program accesses data X & evicts data Y
Capacity miss when access Y again
How to choose Y to minimize chance of needing it again?
Least recently used (LRU) replacement: the least recently used block in a set evicted

## Slide 43: Types of Misses
Compulsory: first time data accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to same location in cache
Miss penalty: time it takes to retrieve a block from lower level of hierarchy

## Slide 44: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)

## Slide 45: Cache Summary
What data is held in the cache?
  Recently used data (temporal locality)
  Nearby data (spatial locality)
How is data found?
  Set is determined by address of data
  Word within block also determined by address
  In associative caches, data could be in one of several ways
What data is replaced?
  Least-recently used way in the set

## Slide 46: Miss Rate Trends
Bigger caches reduce capacity misses
Greater associativity reduces conflict misses

## Slide 47: Miss Rate Trends
Bigger blocks reduce compulsory misses
Bigger blocks increase conflict misses

## Slide 48: Multilevel Caches
Larger caches have lower miss rates, longer access times
Expand memory hierarchy to multiple levels of caches
Level 1: small and fast (e.g. 16 KB, 1 cycle)
Level 2: larger and slower (e.g. 256 KB, 2-6 cycles)
Most modern PCs have L1, L2, and L3 cache

## Slide 49: Intel Pentium III Die

## Slide 50: Virtual Memory
Gives the illusion of bigger memory
Main memory (DRAM) acts as cache for hard disk

## Slide 51: Memory Hierarchy
Physical Memory: DRAM (Main Memory)
Virtual Memory: Hard drive
  Slow, Large, Cheap

## Slide 52: Hard Disk
Takes milliseconds to seek correct location on disk

## Slide 53: Virtual Memory
Virtual addresses
  Programs use virtual addresses
  Entire virtual address space stored on a hard drive
  Subset of virtual address data in DRAM
  CPU translates virtual addresses into physical addresses (DRAM addresses)
  Data not in DRAM fetched from hard drive
Memory Protection
  Each program has own virtual to physical mapping
  Two programs can use same virtual address for different data
  Programs don’t need to be aware others are running
  One program (or virus) can’t corrupt memory used by another

## Slide 54: Cache/Virtual Memory Analogues
Cache | Virtual Memory
Block | Page
Block Size | Page Size
Block Offset | Page Offset
Miss | Page Fault
Tag | Virtual Page Number
Physical memory acts as cache for virtual memory

## Slide 55: Virtual Memory Definitions
Page size: amount of memory transferred from hard disk to DRAM at once
Address translation: determining physical address from virtual address
Page table: lookup table used to translate virtual addresses to physical addresses

## Slide 56: Virtual & Physical Addresses
Most accesses hit in physical memory
But programs have the large capacity of virtual memory

## Slide 57: Virtual Memory Example
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes

## Slide 58: Virtual Memory Example
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Organization:
  Virtual address: 31 bits
  Physical address: 27 bits
  Page offset: 12 bits
  # Virtual pages = 231/212 = 219 (VPN = 19 bits)
  # Physical pages = 227/212 = 215 (PPN = 15 bits)

## Slide 59: Virtual Memory Example
19-bit virtual page numbers
15-bit physical page numbers

## Slide 60: Address Translation

## Slide 61: How to perform translation?
Page table
  Entry for each virtual page
  Entry fields:
    Valid bit: 1 if page in physical memory
    Physical page number: where the page is located

## Slide 62: Page Table Example
VPN is index into page table

## Slide 63: Page Table Example 1
What is the physical address of virtual address 0x5F20?

## Slide 64: Page Table Example 1
What is the physical address of virtual address 0x5F20?
  VPN = 5
  Entry 5 in page table VPN 5 => physical page 1
  Physical address: 0x1F20

## Slide 65: Page Table Example 2
What is the physical address of virtual address 0x73E0?

## Slide 66: Page Table Example 2
What is the physical address of virtual address 0x73E0?
  VPN = 7
  Entry 7 is invalid
  Virtual page must be paged into physical memory from disk

## Slide 67: Page Table Challenges
Page table is large
  usually located in physical memory
Load/store requires 2 main memory accesses:
  one for translation (page table read)
  one to access data (after translation)
Cuts memory performance in half
  Unless we get clever…

## Slide 68: Translation Lookaside Buffer (TLB)
Small cache of most recent translations
Reduces # of memory accesses for most loads/stores from 2 to 1

## Slide 69: TLB
Page table accesses: high temporal locality
  Large page size, so consecutive loads/stores likely to access same page
TLB
  Small: accessed in < 1 cycle
  Typically 16 - 512 entries
  Fully associative
  > 99 % hit rates typical
  Reduces # of memory accesses for most loads/stores from 2 to 1

## Slide 70: Example 2-Entry TLB

## Slide 71: Memory Protection
Multiple processes (programs) run at once
Each process has its own page table
Each process can use entire virtual address space
A process can only access physical pages mapped in its own page table

## Slide 72: Virtual Memory Summary
Virtual memory increases capacity
A subset of virtual pages in physical memory
Page table maps virtual pages to physical pages – address translation
A TLB speeds up address translation
Different page tables for different programs provides memory protection

## Slide 73: Memory-Mapped I/O
Processor accesses I/O devices just like memory (like keyboards, monitors, printers)
Each I/O device assigned one or more address
When that address is detected, data read/written to I/O device instead of memory
A portion of the address space dedicated to I/O devices

## Slide 74: Memory-Mapped I/O Hardware
Address Decoder:
  Looks at address to determine which device/memory communicates with the processor
I/O Registers:
  Hold values written to the I/O devices
ReadData Multiplexer:
  Selects between memory and I/O devices as source of data sent to the processor

## Slide 75: The Memory Interface

## Slide 76: Memory-Mapped I/O Hardware

## Slide 77: Memory-Mapped I/O Code
Suppose I/O Device 1 is assigned the address 0xFFFFFFF4
  Write the value 42 to I/O Device 1
  Read value from I/O Device 1 and place in $t3

## Slide 78: Memory-Mapped I/O Code
Write the value 42 to I/O Device 1 (0xFFFFFFF4)
  addi $t0, $0, 42
  sw $t0, 0xFFF4($0)

## Slide 79: Memory-Mapped I/O Code
Read the value from I/O Device 1 and place in $t3
  lw $t3, 0xFFF4($0)

## Slide 80: I/O Systems
Embedded I/O Systems
  Toasters, LEDs, etc.
PC I/O Systems

## Slide 81: Embedded I/O Systems
Example microcontroller: PIC32
  Microcontroller
  32-bit MIPS processor
  Low-level peripherals include:
    Serial ports
    Timers
    A/D converters

## Slide 82: Digital I/O
// C Code
#include <p3xxxx.h>
int main(void) {
int switches;
TRISD = 0xFF00; // RD[7:0] outputs
// RD[11:8] inputs
while (1) {
// read & mask switches, RD[11:8]
switches = (PORTD >> 8) & 0xF;
PORTD = switches; // display on LEDs
}
}

## Slide 83: Serial I/O
Example serial protocols
  SPI: Serial Peripheral Interface
  UART: Universal Asynchronous Receiver/Transmitter
  Also: I2C, USB, Ethernet, etc.

## Slide 84: SPI: Serial Peripheral Interface
Master initiates communication to slave by sending pulses on SCK
Master sends SDO (Serial Data Out) to slave, msb first
Slave may send data (SDI) to master, msb first

## Slide 85: UART: Universal Asynchronous Rx/Tx
Configuration:
  start bit (0), 7-8 data bits, parity bit (optional), 1+ stop bits (1)
  data rate: 300, 1200, 2400, 9600, …115200 baud
Line idles HIGH (1)
Common configuration:
  8 data bits, no parity, 1 stop bit, 9600 baud

## Slide 86: Timers
// Create specified ms/us of delay using built-in timer
#include <P32xxxx.h>
void delaymicros(int micros) {
if (micros > 1000) { // avoid timer overflow
delaymicros(1000);
delaymicros(micros-1000);
}
else if (micros > 6){
TMR1 = 0; // reset timer to 0
T1CONbits.ON = 1; // turn timer on
PR1 = (micros-6)*20; // 20 clocks per microsecond
// Function has overhead of ~6 us
IFS0bits.T1IF = 0; // clear overflow flag
while (!IFS0bits.T1IF); // wait until overflow flag set
}
}
void delaymillis(int millis) { while (millis--) delaymicros(1000); // repeatedly delay 1 ms
} // until done

## Slide 87: Analog I/O
  Needed to interface with outside world
Analog input: Analog-to-digital (A/D) conversion
  Often included in microcontroller
  N-bit: converts analog input from Vref--Vref+ to 0-2N-1
Analog output:
  Digital-to-analog (D/A) conversion
    Typically need external chip (e.g., AD558 or LTC1257)
    N-bit: converts digital signal from 0-2N-1 to Vref--Vref+
  Pulse-width modulation

## Slide 88: Pulse-Width Modulation (PWM)
Average value proportional to duty cycle
Add high-pass filter on output to deliver average value

## Slide 89: Other Microcontroller Peripherals
Examples
  Character LCD
  VGA monitor
  Bluetooth wireless
  Motors

## Slide 90: Personal Computer I/O Systems
USB: Universal Serial Bus
  USB 1.0 released in 1996
  standardized cables/software for peripherals
PCI/PCIe: Peripheral Component Interconnect/PCI Express
  developed by Intel, widespread around 1994
  32-bit parallel bus
  used for expansion cards (i.e., sound cards, video cards, etc.)
DDR: double-data rate memory

## Slide 91: Personal Computer I/O Systems
TCP/IP: Transmission Control Protocol and Internet Protocol
  physical connection: Ethernet cable or Wi-Fi
SATA: hard drive interface
Input/Output (sensors, actuators, microcontrollers, etc.)
  Data Acquisition Systems (DAQs)
  USB Links